## Slide 1: Survey of Methods for Model Order Reduction For Seminar High Dimensional Methods in Scientific Computing
Evgeni Todorov
Technical University of Munich
Department of Informatics
Munich, June 2021

## Slide 2: Contents
Introduction
– What is MOR and why we do it?
Example
– Illustration of using MOR in structural mechanics
Highlights
– Overview of some important or up-and-coming methods
Application
– Wide selection of interesting recent examples
Conclusion
– The way forward

## Slide 3: Model Order Reduction
Model: Useful representation of reality
Order: For mathematical models, the number of degrees of freedom
  – Closely related to computational intensity
Reduction: Describe the same reality with less effort

## Slide 4: Model Order Reduction - Future
Classically for large-scale simulation (weather, physics, etc.)
Increasingly applied to efficient simulation:
  Real-time:
  – Control systems
  – Internet of Things
  Many-query:
  – Design optimization
  – Parameter estimation
  Outer-loop:
  – Uncertainty quantification
  – Advanced metrology
Measure
Fit
Simulate
Predict
Effect

## Slide 5: Example: Structural Mechanics

## Slide 6: Example: Component Mode Synthesis
Typical industry-standard reduction method for mechanical systems
Implemented in commercial packages (e.g. NASTRAN and ANSYS)
Example of a hybrid modal reduction method
Projection along physical and modal coordinate basis vectors
Substructuring = Superelements

## Slide 7: Example: Component Mode Synthesis

## Slide 8: Example: Substructuring

## Slide 9: Example: Craig-Bampton transformation
interior
boundary
Constraint modes
eigenvector
Fixed boundary modes
eigenvectors matrix

## Slide 10: Highlights: Algorithm and Data-driven

## Slide 11: Algorithm-driven methods
Multigrid (and algebraic multigrid) methods
Adaptive mesh (and algorithm) control
Multiscale modelling
Subject of multiple CSE courses
Proper Generalized Decomposition (PGD)
Ibeid, Huda & Olson, Luke & Gropp, William. (2018). FFT, FMM, and Multigrid on the Road to Exascale: performance challenges and opportunities. https://arxiv.org/abs/1605.01522

## Slide 12: Data-driven methods
Proper Orthogonal Decomposition (POD)
(closely related to Principal Component Analysis)
SVD
CC-BY
Wikimedia/ File:GaussianScatterPCA.svg

## Slide 13: Data-driven methods
Empirical Interpolation method (EIM)
– Computing non-linear component with POD is expensive
– Interpolate it instead
– Discrete EIM (DEIM) uses greedy algorithm to find permutation matrix P
1. Start with the column maximum of (non-orthogonal space) U
2. Compute a residual from the decomposition
3. Get the maximum index of the residual
4. Repeat from 2. until done
– More efficient for the non-linear component

## Slide 14: Data-driven methods
Non-linear machine learning approaches
– Diffusion maps and other manifold learning
– Neural networks
Koopman Operator-based methods
– Observable
– Spectral decomposition for MOR (e.g. DMD)

## Slide 15: Applications

## Slide 16: Application – Aeroelastic Analysis
Coupling of aerodynamic effects to the structural response
Obtain loads
GFEM vs stick model vs ROM
N/A: Galerkin projection, modal decomposition, POD
Parametric techniques:
Aero-structural design loop

## Slide 17: Application: Control of Soft Robots
Heavy offline stage
Real-time interaction for control system design
Real-time calculation in the control loop
ROM – more efficient than coarse mesh

## Slide 18: Application: Cardiovascular System Modeling
Shear stress in carotid artery bifurcation
– POD + DEIM
– Parametrized Navier-Stokes
– Stensosis (obstruction)
– Input flow rate
Cardiac electrophysiology activation map
– POD + DEIM
– 9 parameters:
electrical conductivity and ionic dynamics
CC-BY-NC-ND

## Slide 19: Conclusion
Very robust methods for dealing with linear systems
Parametric modelling relevant to real-time, many-query, outer-loop:
  multidisciplinary optimization
  digital twins
  autonomous control systems
  augmented reality
  data rich measurements
Data-driven and non-linear MOR – active research field related to machine learning
Gap between scientific advancement and industrial practice

## Slide 20: Further reading
Expected soon

## Slide 22: Extra Slides

## Slide 23: Proper Orthogonal Decomposition (POD)
SVD

## Slide 24: Data-driven example: Earth Geopotential Model
CC-BY Ince, E. S., Barthelmes, F., Reißland, S., Elger, K., Förste, C., Flechtner, F., and Schuh, H.: ICGEM – 15 years of successful collection and distribution of global gravitational models, associated services, and future plans, Earth Syst. Sci. Data, 11, 647–674, DOI:10.5194/essd-11-647-2019
Model the Earth gravitational field
In terms of spherical harmonics
Based on very large number of data-points
(actually series of models)

## Slide 25: Application: Structural Health Monitoring
Parametric Reduced Order Model
Model situation for damage identification from photographs
Reduced order model used to train a Machine Learning classifier